## Slide 1: Introduction to Modeling Performance and Verification with Synthesizable MatchLib
Stuart Swan | Platform Architect
Siemens EDA, a part of Siemens Digital Industries Software

## Slide 2: What is MatchLib?
MatchLib is a SystemC library of commonly used functions and components developed in partnership with NVIDIA
  Interfaces, FIFOs, interconnect, etc.
Allows most design and verification of SoCs to be performed in SystemC
  Verify system-level performance earlier
  30x faster than RTL for timing-accurate simulation
  Easily plugs into existing DV flows
Enables control-oriented design
  Easy-to-use throughput accurate modelling
  DMA, Arbiters, Bus I/F
MatchLib
*.h
Users
SystemC
Design
Catapult
HLS
RTL
Performance Validation / Verification
SystemC or System Verilog
Test Bench

## Slide 3: MatchLib + HLS Enables an Efficient Verification Flow
MatchLib Involves DV Team at Every Stage of the Design Process
  Early access to HW
Smaller, faster models
  C++/SystemC model is typically about 1/10 or less than the size of the RTL model
  Easy to verify and debug
C++/SystemC testbench reuse
  Catapult makes it possible to automatically use same testbench for SystemC and Verilog models
You can put thin Verilog wrapper around SystemC DUT
  If using SV UVM DV flow, enables SV DV effort to start much earlier (even before any HLS)
SystemC or System Verilog
Test Bench
DUT
SystemC or RTL Verification
RTL, SystemC, or C++ with MatchLib wrapper

## Slide 4: MatchLib Reduces Risks in Modern Digital Design
Today's HW designs often process huge sets of data, with large intermediate results.
  Machine Learning, Computer Vision, 5G Wireless
Hard part is often managing the movement of data in the chip across all scenarios
  Memory/interconnect architecture often has more impact on power/performance than the design of the computation units themselves
Evaluating and verifying memory/interconnect architecture at RTL level is often not feasible
  Too late in design cycle
  Too much work to evaluate multiple candidate architectures
  The most difficult/costly HW (& HW/SW) problems are found during system integration
  If integration first occurs in RTL, it is very late and problems are very costly
MatchLib + SystemC HLS lets integration occur early when fixing problems is much cheaper
AXI4 Router/
Splitter
AXI4 Router/
Splitter
AXI4
Arbiter
AXI4
Arbiter
DMA0
DMA1
AXI4 Router/
Splitter
MatchLib AXI4 Fabric
RAM0
RAM1
CPU
Bus contention
MatchLib AXI4 Fabric SystemC Simulation

## Slide 5: Using MatchLib Connections
MatchLib’s Connections is a library and API of latency-insensitive channels
All components of this library are synthesizable using HLS
Connections library consists of ports and channels
  Port implements data/ready/valid protocol
Connections are templatized for data type T
dat
rdy
val
dat
rdy
val
dat
rdy
val

## Slide 6: Using MatchLib Connections - Example
private: void main() {
out1.Reset();
in1.Reset();
wait();
#pragma hls_pipeline_init_interval 1
#pragma pipeline_stall_mode flush
while (1) {
uint32_t t = in1.Pop();
out1.Push(t + 0x100);
}
}
};
#include <mc_connections.h>
class dut : public sc_module {
public:
sc_in<bool> CCS_INIT_S1(clk);
sc_in<bool> CCS_INIT_S1(rst_bar); Connections::Out<uint32> CCS_INIT_S1(out1);
Connections::In <uint32> CCS_INIT_S1(in1);
SC_CTOR(dut) {
SC_THREAD(main);
sensitive << clk.pos();
async_reset_signal_is(rst_bar, false);
}
Connections inputs and outputs
Connections write
Connections read

## Slide 7: Simulating Performance Before Synthesis
Pre-HLS and Post-HLS simulation throughput are the same
There can be differences in latency
Pre-HLS Simulation
Post-HLS Simulation

## Slide 8: Modelling Bus I/F With MatchLib
MatchLib provides high-quality implementations of AXI4 master and slave interfaces
Users can also model custom bus interfaces using MatchLib
  This example models a simple read bus I/F with burst
  Testbench models 2-cycle overhead for initiating a new burst
class dut : public sc_module {
public:
… void main() {
wait();
#pragma hls_pipeline_init_interval 1
#pragma pipeline_stall_mode flush
while (1) {
go.sync_in();
uint32 addr = addr_offset_csr.read();
uint32 burst_size = burst_csr.read();
read_addr_chan.Push(addr);
read_burst_size.Push(burst_size);
do {
uint32 data = read_data_chan.Pop();
read_data_out.Push(data);
} while (--burst_size !=0);
}
Initiate a burst by sending address and burst size
Read “burst_size” data from bus I/F

## Slide 9: Modelling Bus I/F With MatchLib
Small burst size and/or non-consecutive addresses will hurt performance by injecting dead cycles
Pre-HLS Simulation
Initiate a burst by sending address and burst size
Burst runs with throughput==1
2-cycle overhead to start new burst

## Slide 10: Complex Bus Protocols are Easily Modelled with MatchLib
  AXI4 Master and Slaves are part of the MatchLib library
    AXI4 segmenter transparently manages burst size, 4k boundaries, etc
  AXI4 Read Master I/F with built-in segmentation
    r_master<>
    AXI4 Write Master I/F with built-in segmentation
    w_master<>
    AXI4 Slave I/F with built-in segmentation
    slave<>
  Interface reads/writes use connections Push/Pop methods
class bus_if: public sc_module
…
r_master<> r_master0;
…
while (1) {
…
r_payload r = r_master0.r.Pop();
…
}
…

## Slide 11: MatchLib and Catapult HLS Results
Notes: Nvidia performed most verification at the SystemC level and simulation speed was 30 times faster than RTL
Nvidia has taped out multiple chips that were almost entirely designed with this flow.

## Slide 12: Recap: MatchLib and Catapult HLS Enable Modern D/V Flow
  Designer focuses on chip architecture, functionality, and throughput analysis/verification.​
    HLS adds pipelining, optimizes microarchitecture, provides fully automated flow to placed gates.​
  Focus of verification effort moves to C++/SystemC level, enabling much greater efficiency.​
  Siemens Catapult HLS team is ready to help design teams adopt and succeed with MatchLib​
    Fixes and enhancements to MatchLib source code​
    Examples, assistance​
Notes: Designer focuses on chip architecture, functionality, and throughput analysis/verification.
Focus of verification effort moves to C++/SystemC level, enabling much greater efficiency.
Mentor Catapult HLS team is ready to help design teams adopt and succeed with MatchLib

## Slide 13: SystemC / Matchlib Resources in Catapult Release
Matchlib training slides
$MGC_HOME/shared/examples/matchlib/toolkit/doc/matchlib_customer_training.ppt
Matchlib example kit in Catapult install
$MGC_HOME/shared/examples/matchlib/toolkit

## Slide 14: External Catapult SystemC / Matchlib Resources
Catapult SystemC MatchLib On-Demand Training (ODT)
https://eda.learn.sw.siemens.com/training/courses/catapult-high-level-synthesis-library
2021 Catapult Virtual Seminar (ML Accelerator using Matchlib):
https://event.on24.com/wcc/r/3187802/BF0CAE586A768CDB1314C956F64ABA35
Catapult Matchlib Webinars:
https://webinars.sw.siemens.com/how-matchlib-and-systemc-enables
https://webinars.sw.siemens.com/nvidia-design-and-verification-of-a-1
https://webinars.sw.siemens.com/early-axi-soc-performance
Youtube video from NVidia:
https://www.youtube.com/watch?v=n8_G-CaSSPU
Accellera SystemC Evolution Day 2020 Matchlib Presentation and Open Source Example Kit:
https://forums.accellera.org/files/category/2-systemc/

## Slide 15: Thank you!